## Slide 1: Quantifying Coastal Storm and Sea Level Rise Risks to Naval Station Norfolk (SERDP RC-1701)
Ms. Kelly A. Burks-Copes
Environmental Laboratory
US Army Engineer Research
and Development Center
Vicksburg, MS
30 October 2013

## Slide 2: Case Study: Quantifying Coastal Storm and Sea Level Rise Risks to Naval Station Norfolk (SERDP RC-1701)
Problem Statement
  Devise and demonstrate a rigorous yet flexible systems-scale approach
  Quantitatively evaluate natural hazard risks to critical military assets (i.e., infrastructure) and mission capabilities
  Address a range of SLR, tidal fluctuation, and storm stage-frequencies
Technical Goals
  Characterize impacts
  Decompose mission & infrastructure systems
  Pinpoint vulnerabilities
  Quantify performance sustainability risks
  Identify adaptive capacity tipping points
  Communicate results to field
IPCC 2013
NRC 1987
USACE 2011

## Slide 3: Technical Approach
  Prescribed SERDP scenarios are reasonably supported in the peer reviewed literature
This is a Demonstration Project –
  Select missions, capabilities, assets, hazards, and forcings are modeled
  Coastal storm parameters are not altered due to potential climate change effects
Datums
  Horizontal datum = North American Datum of 1983 (NAD83)
  Vertical datum = North American Vertical Datum of 1988 (NAVD 88)
Period of Analysis
  Start Date = 2000
  End Date = 2100 (100 yr period of analysis)
Sea Level Rise
(local MSL between 2000-2100)
  0.5m
  1.0m
  1.5m
  2.0m
Storm Return Intervals
Boon (2012)
Ezer and Corlett (2012)
Recurrence interval | Probability of occurrence in any given year | Percent chance of occurrence in any given year
100-yr | 1 in 100 | 1%
50-yr | 1 in 50 | 2%
10-yr | 1 in 10 | 10%
1-yr | 1 in 1 | 100%

## Slide 4
RISK OF MISSION IMPAIRMENT
Asset Capability Network Development – Infrastructure Network
(ArcGIS)
Structural Analysis
(ISS3D + HAZUS MR-4)
ASSET IDENTITY,
CHARACTERISTICS
AND CONNECTIVITTY
Geomorphic and Geologic Assessment
Ecology and Land Use Conversion Assessment
(Straight-line & SLAMM)
Regional Surge and Waves Assessment
(TC96 + ADCIRC + SWAN)
Nearshore Waves , Current, Water Levels, and Sediment Transport Assessment
(CMS)
Surface Flood Routing
(GSSHA)
Shoreline characterization
Bathymetry and land cover changes
SLR Scenario- and event-based time history of surge, waves & wind
Water level, waves, and morphology changes
Groundwater Assessment
(AdH)
Groundwater table position
SLR Scenario (0, 0.5, 1, 1.5, 2m)
Risk Assessment
(Netica)
Probability
of the
damage states
given the loadings
WATER DEPTH AND DURATION
Max IMUM Water Level, Wave HEIGHT, Current Speed, EROSION, Accretion, & SEDIMENT Transport Rate
MAXIMUM WIND,
SURGE, & WAVES
Tiered Risk Assessment Approach:
  Step 1: Site Selection
  Step 2: Regional Assessment
  Step 3: Installation Specific Assessment
Notes: Notes:
This is an animated slide that will run on its own. . . . The blue boxes are the models we deployed . . . . They provide “forcings” in red that “push” against the infrastructure. The green boxes are the asset decomp & the structural analysis . . . They provide the “fragility” of each asset system . . . the probability of the storms and the fragility of the infrastructure are combined & the probability o f mission performance is assessed in the Bayesian network.
The demo site for the study was Naval Station Norfolk (Virginia, USA), but the coastal storm analysis covered the Chesapeake Bay area. . . . We conducted a “tiered” analysis at the North Atlantic, Regional (Hampton Roads Area), and Local (NNS) scales.
All models deployed were either open source or ERDC-developed.
It took more than 22 researchers with varied backgrounds in coastal modeling, engineering and risk assessment to get the job done.
We analyzed 500+ FEMA-derived simulated hurricanes to conduct the study, and selected “representatives of the 1, 10, 50 & 100 year events to focus our efforts – we also included a Nor’easter at the request of the naval base.
Model outputs:
  Straight-line & SLAMM captured inundation due to SLR
  ADCIRC/SWAN/TC96 handled hurricane simulation
  CMS incorporated bathymetry, wave run-up, sediment transport & tides
  GSSHA & AdH/WASH123D incorporated infiltration, flood routing & precipitation
We decomposed the mission (into capabilities & critical assets) and focused the analysis on infrastructure systems such as electricity wastewater, steam, etc.
Structural analysis of these systems was conducted to generate fragility curves to assess system vulnerability to storm forcings (winds, waves, surge, inundation)
We used a Bayesian network to combine the “forcings” from the storms with asset fragility and interconnectivity to assess probabilistic mission failure.
More than 13,000 conditional probabilities were computed.

## Slide 5: Regional Assessments
Hurricane tracks impacting the project region.
Maximum wind speed in miles per hour for
Hurricane 449
^Videos 2012\1_SLAMM.ppsx
Geomorphological Assessment
  Modeled geomorphic evolution as sea levels rise
  Inventory natural and engineered coastal features
  Assess stability of features as sea levels rise
  Provided inputs on base conditions in the bay for sediment transport modeling
Ecological Assessment
  Sea Level Affecting Marsh Model (SLAMM)
  Biome Shifts
  Open Water Surface Increases
Coastal Storm Simulations
  Used Joint Probability Method with Optimal Sampling (JPM-OS) for storm parameterization
    Nor’easters included (3 total)
    Parameters:
      Cp (central pressure)
      Rmax (radius of maximum winds)
      Tracks / heading
      Vf (forward speed)
      Holland B (landfall decay)
    Wind Forcings using TC96 Model
    Envelope of maximum wind speed
    Inputs to circulation and wave models at both region and nearshore scales
    Storm parameters not modified to reflect climate change
    Same wind fields used for modeling in all SLR scenarios
Notes: Geomorphological Assessment
  Modeled geomorphic evolution as sea levels rise
  Inventory natural and engineered coastal features
  Assess stability of features as sea levels rise
  Provided inputs on base conditions in the bay for sediment transport modeling
Ecological Assessment
  Used SLAMM – Sea Level Rise Affecting Marsh Model
  Regional Storm Modeling
    Used Joint Probability Method with Optimal Sampling (JPM-OS) for storm parameterization
      Used subset of 460 synthetic hurricanes to produce 50- and 100-yr approx water levels (17 total)
      Nor’easters included (3 total)
      Parameters:
        Cp (central pressure)
        Rmax (radius of maximum winds)
        Tracks / heading
        Vf (forward speed)
        Holland B (landfall decay)
  Wind Forcings using TC96 Model
    Envelope of maximum wind speed
    Inputs to circulation and wave models at both region and nearshore scales
    Storm parameters not modified to reflect climate change
    Same wind fields used for modeling in all SLR scenarios

## Slide 6: Regional Storm Results
Storm 449 0m SLR (max surge = 3.0 m)
Storm 449 2m SLR (max surge = 5.8 m)
Regional surge/wave water levels were generated for each of the storms with Advanced Circulation (ADCIRC) and Simulating Waves Nearshore (SWAN) models
Models driven using wind fields, considering topo/bathy contours and friction coefficients derived from land cover and interpolated onto the model mesh
100 ADCIRC, SWAN & TC96 Runs Made (17 hurricanes & 3 nor’easters x 5 SLR Scenarios)
Notes: High-resolution spatially-explicit regional coastal flood-stage frequency results are made possible using a proven set of hydrodynamic models and supporting high-performance computing resources at ERDC
ADCIRC provides storm surge elevations across the region, based on principles of conservation of mass and momentum in the movement of coastal storm water
SWAN provides regional significant wind wave heights, periods, directions, and spectra
ADCIRC is run separately from SWAN initially, then ADCIRC is re-run to add in wind-wave radiation stresses to surges for estimating wave setup, and therefore, contributions to water surface elevations on top of surges due to wave action
CMS gets from ADCIRC and SWAN the water levels, as well as significant wind wave heights, periods, directions, and spectra, for the nearshore perimeter around the installation to compute nearshore waves, runup, and overtopping onto the installation
GSSHA gets water levels and flows into the installation from CMS to compute interior flood routing and stages on the installation

## Slide 7: Surface Flood Routing – Gridded Surface-Subsurface Hydraulic Assessment (GSSHA)
1-yr Storm
10-yr Storm
0.0 m SLR
0.5 m SLR
1.0 m SLR
1.5 m SLR
2.0 m SLR
50-yr Storm
100-yr Storm
Nor’easter

## Slide 9: Infrastructure Vulnerability Assessment

## Slide 10: Asset Network Diagramming
Provide At-Berth Support
Provide
Water
Mission
Capability
Asset
Provide Berthing Space
Provide Electric Power
Provide CHT (Sewage, OW)
Provide
Supplies
Provide Steam
Pier #
Steam Plant
Natural Gas Supply
FISC
Warehouses
Sewage and Oily Waste Treatment
Electrical
Transmission System
Water Treatment Plant
Electrical
Substation
Untreated Water Supply
Water Distribution System
Steam Distribution System
Electrical Supply
Provide
Personnel Support
Pier Parking
Areas
Ammunition
Bunkers
Base Road
Network
Off-Base Road
Network
Water Storage
Provide POL
(Fuel, Oil)
POL Storage Tanks
POL Distribution System
Provide Ammunition
POL Supply
Provide Communications
NCTAMS Building
Off-Base
Communications
Commercial Goods Suppliers

## Slide 11: Asset Connectivity
Electrical
Pier 11
Pier 12
Pier 14
Steam
Berthing
Water
Oily Waste

## Slide 12: Utilization of the RC-1701 Approach:
The model is used for inference about the infrastructure system and management.
        Probability of asset damage states and functionality.
        Probability of a loss in capability (service interruption).
        Probability potential losses in mission performance.
        How would alternative system design or retrofits affect mission performance?
        Where should better information on structural reliability be obtained?

## Slide 13: Final Bayesian Network
Storm Severity
Sea Level Rise
Score Card:
217 Nodes (boxes)
  2 Risk drivers
  95 Asset damage
  97 Function
  23 Capability
  3 Mission performance
437 Edges (lines)
13,068 Probabilities

## Slide 14: Final Risk Assessment Results
Loss in Mission Performance
Service Interruption
Loss in Capability
Tipping point is between 0.5 and 1.0 m SLR.

## Slide 15: Future Directions for Client-Partnering
Portable, Scalable Approach
  Demo Project - NSN Master Planning,
  Adaptive Management (Retrofits),
  Contingency Planning
  Assist with Informing Policy and Planning
  Portfolio Risk Management
  Navy’s Task Force Climate Change
  Worldwide Installation Vulnerability
  Assessment
Dependencies
Outside the Fence Line
  Stakeholders Forum(s)
  Hampton Roads Installations
  VA Recurrent Flooding Study
    (Molly Roggero, VIMS)
Notes: Portfolio Risk Management at a Global Scale – Interdependencies of the bases & how they interact at a global scale to perform the missions
Assist TFCC in developing a high-level vulnerability assessment to come up with the most vulnerable
2. Explicitly evaluate these most vulnerable sites and report back common vulnerabilities and good defensible practices that could be used to update Policy & Guidance.
3. Implicitly provide Engineering Guidance Updates that could be rolled out to the other bases around the world to address CC threats
So what are our next steps – how or when can we get back with you to talk about next steps
Could we get with your working staff and client-partner with them and maybe come back in three months and brief you on our efforts
Allude to the fact that we might have cost-sharing potentials

## Slide 16: Points of Contact
Kelly A. Burks-Copes
  SERDP RC-1701 Project Team Leader
  Environmental Laboratory
  US Army Engineer Research & Development Center
  3909 Halls Ferry Rd., Vicksburg, MS 39180
  Office: 601-634-2290, Mobile: 601-618-5565
  Email: Kelly.A.Burks-Copes@usace.army
Edmond J. Russo, Jr., Ph.D., P.E.
  Chief, Ecosystem Evaluation and Engineering Division
  Environmental Laboratory
  US Army Engineer Research & Development Center
  3909 Halls Ferry Rd., Vicksburg, MS 39180
  Office: 601-634-2067
  Email: Edmond.J.Russo@usace.army