## Slide 1: Sea-Level Rise: Impacts and Responses
Prof. Robert J. Nicholls
Faculty of Engineering and the Environment and
Tyndall Centre for Climate Change Research
University of Southampton
United Kingdom
Email: R.J.Nicholls@soton.ac.uk
Transatlantic Solutions to Sea Level Rise Adaptation: Moving Beyond the Threat
Ted Constant Convocation Center, Old Dominion University, Norfolk, Virginia
October 30-31, 2013

## Slide 2: PLAN
Sea-level rise and its components
Sea-level rise impacts, especially flooding
Sea-level rise responses
  Climate mitigation
  Adaptation
Concluding remarks

## Slide 3
< 1mm/year
6mm/year
> 20mm/year

## Slide 4: Global-Mean Sea-Level Rise: 1700 to 2100 Compiled paleo-sea-level data, tide gauge data, altimeter data, and central estimates and likely ranges for RCP2.6 (blue) and RCP8.5 (red) scenarios
Source: IPCC, 2013, AR5 WG1

## Slide 5: Global Sea-Level Components
Source: IPCC, 2013, AR5 WG1

## Slide 7: Global-Mean Sea-Level Rise: 1700 to 2100 Compiled paleo-sea-level data, tide gauge data, altimeter data, and central estimates and likely ranges for RCP2.6 (blue) and RCP8.5 (red) scenarios
Source: IPCC, 2013, AR5 WG1
?
?
?
?

## Slide 8: Local sea-level components
Where,
∆RSL is the change in relative sea level
∆SLG is the change in global mean sea level
∆SLRM is the regional variation in sea level from the global mean due to meteo-oceanographic factors
∆SLRG is the regional variation in sea level due to changes in the earth’s gravitational field
∆SLRLM is the change in sea level due to vertical land movement
Source: Nicholls et al., 2013 WIRES Climate Change

## Slide 9: Local Sea-Level Rise Norfolk, VA 1962 to 2012 (50 years) – 5.2 mm/yr
Chart: 
| 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
 | 7044 | 6967 | 6991 | 6986 | 7009 | 7043 | 7027 | 7056 | 7056 | 7073 | 7131 | 7101 | 7073 | 7096 | 7012 | 7009 | 7111 | 7088 | 7054 | 7050 | 7087 | 7169 | 7146 | 7105 | 7111 | 7142 | 7068 | 7092 | 7080 | 7142 | 7165 | 7158 | 7104 | 7139 | 7216 | 7212 | 7264 | 7206 | 7172 | 7167 | 7141 | 7213 | 7213 | 7272 | 7230 | 7194 | 7211 | 7279 | 7291 | 7275 | 7281
Data from Permanent Service for Mean Sea Level

## Slide 10: Impacts of Sea-Level Rise
NATURAL SYSTEM EFFECT | 
1. Inundation, flood and storm damage | a. Surge
 | b. Backwater effect
2. Wetland loss (and change) | 
3. Erosion (of ‘soft’ morphology) | 
4. Saltwater Intrusion | a. Surface Waters
 | b. Ground-water
5. Rising water tables/ impeded drainage | 
Source: Nicholls (2010) Book on “Understanding Sea-Level Rise and Variability”

## Slide 11: Flood Case Study: The Solent
Source: Wadey et al., 2012

## Slide 12: Southampton Annual sea levels:1935 to 2010
Mean level
Annual extreme
level
10 March 2008
Trend = 1.4 mm/yr
Trend = 1.2 mm/yr

## Slide 13: Southampton 10 March 2008, high tide

## Slide 14: Yarmouth 10 March 2008, high tide

## Slide 15: Yarmouth 10 March 2008, high tide

## Slide 16: Yarmouth 10 March 2008, high tide

## Slide 17: Yarmouth 29 October 2013, high tide

## Slide 18: Sea level in the English Channel Changes at Newlyn (50cm rise in 100 years)
Notes: Isopleths are lines of sea level rise from 2000 to 2100 at intervals of 10 years. eg Take sea level of 6.5 m above datum at Newlyn. light grey ( in 2000) shows that 6.5m could be exceeded every 100 years,
Whilst in 2100 ( top dark line) 6.5m could be exceeded every 6 months

## Slide 19: Modelled flood events in the Solent Loads & failure mechanisms vs. number of properties flooded
10 March 2008
Source: Wadey et al., 2012

## Slide 20: Port City Locations >1 million population in 2005 (136 locations)
Key global results for the flood plain
40 million people
  0.6% of global population
  (10% of port city population)
US $3000 billion of assets
  5% of global GDP
Port Cities
USA 17 locations
China 14 locations
Brazil 10 locations

## Slide 21: Flood Risk (1) (Hallegatte et al., 2013)
Risk – expected annual losses
Average global coastal flood losses with no adaptation
  $6 billion per year in 2005
  $52 billion per year in 2050 with socio-economic change alone.
  With additional sea-level rise of 20 cm by 2050 and subsidence in susceptible cities, losses rise to $1 trillion per year.
  Conclusion: Adaptation is essential

## Slide 22: Flood Risk (2) (Hallegatte et al., 2013)
Indicative adaptation costs are a few billion US dollars per city in initial investment, plus approximately 2% annual operation and maintenance costs.
This is approximately $50 billion per year for the 136 cities.
When losses do occur, we should expect larger coastal flood disasters than we experience today –due to greater exposure and larger flood depths.

## Slide 23: City Risk Ranking in 2005
Source Hallegatte et al. (2013)

## Slide 24: City Risk Ranking in 2050
Source Hallegatte et al. (2013)

## Slide 25: Climate Mitigation Responses

## Slide 26: Post-2100 Sea-Level Rise Commitment to sea-level rise
Source: IPCC, 2013, AR5 WG1

## Slide 27: Coastal Adaptation

## Slide 28
The Adaptation Process
Klein et al. (1999)
Climate
variability
Coastal
development
objectives
Climate
change
Policy
criteria
Other
stresses
Information,
Awareness
Planning,
Design
Implemen
-
tation
Impacts
Mitigation
Adaptation
Existing
management
practices
Monitoring,
Evaluation

## Slide 29: Planned Adaptation The IPCC Approach
Source: Nicholls (2010) Book on “Understanding Sea-Level Rise and Variability”

## Slide 30: Many Adaptation Options are Available P – Protection; A – Accommodation; R – Retreat.
NATURAL SYSTEM EFFECT |  | POSSIBLE ADAPTATION RESPONSES
1. Inundation, flood and storm damage | a. Surge | Dikes/surge barriers [P], Building codes/floodwise buildings [A], Land use planning/hazard delineation [A/R].
 | b. Backwater effect | 
2. Wetland loss (and change) |  | Land use planning [A/R], Managed realignment/ forbid hard defences [R], Nourishment/sediment management [P].
3. Erosion (of ‘soft’ morphology) |  | Coast defences [P], Nourishment [P], Building setbacks [R].
4. Saltwater Intrusion | a. Surface Waters | Saltwater intrusion barriers [P], Change water abstraction [A/R].
 | b. Ground-water | Freshwater injection [P], Change water abstraction [A/R].
5. Rising water tables/ impeded drainage |  | Upgrade drainage systems [P], Polders [P], Change land use [A], Land use planning/hazard delineation [A/R].
Source: Nicholls (2010) Book on “Understanding Sea-Level Rise and Variability”

## Slide 31: Portfolio of Adaptation Measures for Coastal Cities
Flood warning systems
Subsidence mitigation (in susceptible cities)
Upgraded defences (availability of land)
Flood resilient construction
Land use planning
Disaster preparedness
Source: Nicholls et al., 2008, OECD Report

## Slide 32: Managing Flood Risk Contrasting approaches
Time
2007
2050
2100
more people/property
climate change
ageing FD
Risk
Unacceptable
Tolerable
As low as reasonably possible
Source: Tim Reeder, Environment Agency

## Slide 33: London’s Future Flood Defences

## Slide 34
1m
0m
4m
3m
2m
Max water level rise:
New barrier, retain Thames Barrier, raise defences
Raise Defences
New barrier, raise defences
New barrage
HLO 1
HLO 3a
HLO 3b
HLO 4
HLO 2
Existing system
Improve Thames Barrier and raise d/s defences
Over-rotate Thames Barrier and restore interim defences
Flood storage, improve Thames Barrier, raise u/s & d/s defences
Flood storage, over rotate Thames Barrier, raise u/s & d/s defences
Flood storage, restore interim defences
Previous Extreme
Defra and upper part of new TE2100 likely range
Top of new H++ range
London: Adaptation Pathways
Source: Tim Reeder, Environment Agency

## Slide 35: Concluding Remarks
Sea-level rise is occurring with climate change being a fundamental component;
This is almost certain to accelerate, but with substantial uncertainty and a long timescale;
Sea-level rise exacerbates coastal hazards (e.g., flooding during coastal storms);
Mitigation (global scale) and adaptation (local scale) need to applied together;
Adaptation is an ongoing process, with technical, social and political dimensions;
Planning via adaptation pathways that explicitly include learning is effective to the uncertainties.

## Slide 36: Sea-Level Rise: Impacts and Responses
Prof. Robert J. Nicholls
Faculty of Engineering and the Environment and
Tyndall Centre for Climate Change Research
University of Southampton
United Kingdom
Email: R.J.Nicholls@soton.ac.uk
Transatlantic Solutions to Sea Level Rise Adaptation: Moving Beyond the Threat
Ted Constant Convocation Center, Old Dominion University, Norfolk, Virginia
October 30-31, 2013